92-95 Fuse/Relay Chart

92-95 Relays

| Position | Description | Part # |
| --- | --- | --- |
| I-II | Rear Defroster | 928.615.115.00 |
| III | Not Used (Daytime Running Lights-Canada) |  |
| IV | Foglights | 141.951.253.B |
| V | Starter Relay | 141.951.253.B |
| VI | Not Used |  |
| VII | Headlamp Washers | 928.618.111.00 |
| VIII | Foglight Flasher-Alarm | 141.951.253.B |
| IX | Intensive Washers | 928.618.113.01 |
| X | Ignition Relay-X | 141.951.253.B |
| XI | Intermittent Wiper Delay Timer | 993.615.101.00 |
| XII | Fresh Air (HVAC) Blower | 141.951.253.B |
| XIII | Indicator(turn), 4-Way Flasher | 1H0.953.227 |
| XIV | Defroster | 141.951.253.B |
| XV | ABS Relay | 928.615.124.01 |
| XVI | Twin-Tone Horns | 141.951.253.B |
| XVII | Kick-Down Relay (Auto) 92-93 up to Vin#92PS8 20500 | 928.618.108.00 |
| XVII | Kick-Down Relay (Auto) 93 from VIN#92PS8 20501 to 95 | 928.618.108.01 |
| XVIII | Reverse Light Relay (Auto) | 928.615.114.00 |
| XVIII | Reverse Light Bridge(5-Speed) | 928.615.125.00 |
| XIX | Control Unit – Speedometer | 928.618.221.00 |
| XX | Not Used |  |
| XXI | Interference Noise Suppressor | 928.618.223.00 |
| XXII | EZK Ignition System (w/Fuse Tester) | 928.615.203.00 |
| XXIII-XXIV | Combination Headlamp | 928.618.107.04 |
| XXV | LH-Jetronic Fuel Injection | 141.951.253.B |
| XXVI | Fuel Pump,O2 Sensor | 141.951.253.B |

| Relays Not Located in Fuse/Relay Panel |
| --- |
| Description | Location | Part # |
| Seat Belt / Chime | Inside Center Console Under Radio | 928.618.102.03 |
| Rear Window Wiper | Behind Tool Kit Cover - Drivers Side | 928.618.104.00 |
| Ignition Overheat Relay | Mounted on Engine Computer Frame | 928.618.175.00 |
| Anti-Theft Relay | Inside Center Console Under Radio | 928.637.160.00 |

Superseded Relays:

92861510100 - 99361510101

92861810704 - 92861810764

92861822100 - 96461822102

92861510100 - 99361510101

| 92-95 Fuses |
| --- |
| # | Description | AMP |
| 1 | Dipped(low) Beam – Left | 7.5 |
| 2 | Dipped(low) Beam – Right | 7.5 |
| 3 | Main(High) Beam – Left | 7.5 |
| 4 | Main(High) Beam – Right | 7.5 |
| 5 | Driving Lights | 15 |
| 6 | Fog Lights | 15 |
| 7 | Parking Light - Left | 5 |
| 8 | Parking Light - Right | 5 |
| 9 | Lights: Ashtray, Instruments | 5 |
| 10 | License Plate Lights | 5 |
| 11 | Rear Foglight (Euro only) | 5 |
| 12 | Indicator (Turn) Light - Front/Left | 5 |
| 13 | Indicator (Turn) Light - Rear/Left | 5 |
| 14 | Indicator (Turn) Light - Front/right | 5 |
| 15 | Indicator (Turn) Light - Rear/Left | 5 |
| 16 | Rear Window Defroster | 25 |
| 17 | Warning Flasher, Engine Comp. Light | 15 |
| 18 | Window/Sunroof Regulator | 25 |
| 19 | Headlamp Washing System | 25 |
| 20 | Fresh Air Blower | 30 |
| 21 | Radio - Amplifier | 15 |
| 22 | Electric Seat Adjustment - Left | 30 |
| 23 | Electric Seat Adjustment - Right | 30 |
| 24 | Horns | 15 |
| 25 | Diagnostic Connector,Current Pulse-Tailgate, Interior lights | 7.5 |
| 26 | Tailgate Release | 1 |
| 27 | Headlamp Motor | 15 |
| 28 | Antilock Braking System | 15 |
| 29 | Radiator Cooling Fan #1 | 30 |
| 30 | Radiator Cooling Fan #2 | 30 |
| 31 | Not Used |  |
| 32 | Not Used |  |
| 33 | Cigarette Lighter | 25 |
| 34 | Windshield Wipers, Washer Jet Heating | 25 |
| 35 | Brake Light, Cruise Control | 7.5 |
| 36 | Control Unit - Cooling Fans | 5 |
| 37 | Air Conditioning | 7.5 |
| 38 | Fuel Pump, O2 Sensor-Heating | 15 |
| 39 | Instruments, Kick-down, Warning Lights, Switch for Rear Wiper | 5 |
| 40 | Reverse Lights, Mirror Motors, RDK System | 7.5 |
| 41 | Light: Light Switch, Button Panel, Interior Light Delay, Diag. Con. | 5 |
| 42 | Rear Window Wiper | 7.5 |
| 43 | Telephone (Factory) | 7.5 |
| 44 | Seat Heating | 15 |
| 45 | Supplementary A/C (Rear A/C) | 15 |

Fuses counted Left to Right 1-45 across the top of Fuse/Relay Panel

# Text boxes

XV

ABS

IV

Fog

XVIII

Rev.

XXIII     XXIV

CombHeadlamp

XXI

Noise

XIX

FCU

XVII

Kick

XIII

Turn

XI

Wiper

IX

-----

VIII

Flash

VII

Hwash

V

Start

I                 II

Rear defroster

III

-- (drl)

X

X-ign

XII

HVAC

XX

-----

VI

-----

XIV

defrost

XXII

EZK

XXVI

Fuel

XVI

Horn

XXV

LH